## Slide 1: Number systems
By Krishna Chakravarty
Associate Professor
KIIT Deemed to be University

## Slide 2: contents
Introduction
Decimal number system
Binary number systems
Octal number system
Hexadecimal number system
Conversions to decimal
Conversions from decimal
Other conversions and shortcuts
Binary arithmatics
Day 3

## Slide 3: introduction
When we type some letters or words, the computer translates them in numbers as computers can understand only numbers.
The value of each digit in a number can be determined using −
  The digit
  The position of the digit in the number
  The base of the number system

## Slide 4: Base , weighting factor
  BASE or Radix
  In mathematical numeral systems, the radix or base is the number of unique digits, including zero, used to represent numbers in a positional numeral system. For example, for the decimal system (the most common system in use today) the radix is ten, because it uses the ten digits from 0 through 9.
  Base 2 : 0 and 1
  Base 8 : 0, 1, 2, 3, 4, 5, 6, 7
  Base 10 : 0, 1, 2, 3, 4, 5, 6, 7, 8, 9
  Weighting factor
  Weight of a respective position. I
  In decimal form, weight of each digit increases by a factor of 10 as one moves to the left.
  754 = 7*100 + 5 *10 + 4

## Slide 5: Decimal Number systems
Decimal Number System
Decimal number system has base 10 as it uses 10 digits from 0 to 9.
In decimal number system, the successive positions to the left of the decimal point represent units, tens, hundreds, thousands, and so on.
Each position represents a specific power of the base (10). For example, the decimal number 1234 consists of the digit 4 in the units position, 3 in the tens position, 2 in the hundreds position, and 1 in the thousands position. Its value can be written as
    1234
    =1000 + 200 + 30 + 4
    = (1 x 1000)+ (2 x 100)+ (3 x 10)+ (4 x l)
    =(1 x 103)+ (2 x 102)+ (3 x 101)+ (4 x l00)

## Slide 6: Computer number systems
S.No. | Number System and Description
1 | Binary Number System Base 2. Digits used : 0, 1
2 | Octal Number System Base 8. Digits used : 0, 1, 2, 3, 4, 5, 6, 7
3 | Hexa Decimal Number System Base 16. Digits used: 0 , 1, 2, 3, 4, 5, 6, 7, 8, 9, Letters used : A, B, C, D, E, F

## Slide 7: BINARY number SYSTEM
Characteristics of the binary number system are as follows −
Uses two digits, 0 and 1
Also called as base 2 number system
First position in a binary number represents a 0 power of the base (2). Example 20
Last position in a binary number represents a x power of the base (2). Example 2x where x represents the last position - 1.
  101010 binary
  =( 32*1) + (16*0) + (8*1) +(4*0) + (2*1) + 1*0)
  = 32 +8 + 2 = 42
1 | 0 | 1 | 0 | 1 | 0
25 | 24 | 23 | 22 | 21 | 20
32 | 16 | 8 | 4 | 2 | 1

## Slide 8: BINARY number SYSTEM
Example
Binary Number: 101012
Calculating Decimal Equivalent −
Note − 101012 is normally written as 10101.
Step | Binary Number | Decimal Number
Step 1 | 101012 | ((1 x 24) + (0 x 23) + (1 x 22) + (0 x 21) + (1 x 20))10
Step 2 | 101012 | (16 + 0 + 4 + 0 + 1)10
Step 3 | 101012 | 2110

## Slide 9: octal number SYSTEM
Characteristics of the octal number system are as follows −
Uses eight digits, 0,1,2,3,4,5,6,7
Also called as base 8 number system
First position in an octal number represents a 0 power of the base (8). Example 80
Last position in an octal number represents a x power of the base (8). Example 8x where x represents the last position – 1
2 | 3 | 5
2*82 | 3*81 | 5*80
2*64 | 3*8 | 5*1
128 | 24 | 5
Octal 235
= decimal (32 + 24 + 5)
= decimal 157

## Slide 10: octal number SYSTEM
Example
Octal Number: 125708
Calculating Decimal Equivalent −
Step | Octal Number | Decimal Number
Step 1 | 125708 | ((1 x 84) + (2 x 83) + (5 x 82) + (7 x 81) + (0 x 80))10
Step 2 | 125708 | (4096 + 1024 + 320 + 56 + 0)10
Step 3 | 125708 | 549610

## Slide 11: hexadecimal number SYSTEM
Characteristics of the hexadecimal number system are as follows
Uses 10 digits and 6 letters, 0, 1, 2, 3, 4, 5, 6, 7, 8, 9, A, B, C, D, E, F
Letters represent the numbers starting from 10. A = 10. B = 11, C = 12, D = 13, E = 14, F = 15
Also called as base 16 number system
First position in a hexadecimal number represents a 0 power of the base (16). Example, 160
Last position in a hexadecimal number represents a x power of the base (16). Example 16x where x represents the last position – 1

## Slide 12: hexadecimal number SYSTEM
Hexadecimal Number: 19FDE16
Calculating Decimal Equivalent −
Note − 125708 is normally written as 12570..
Step | Hexa Number | Decimal Number
Step 1 | 19FDE16 | ((1 x 164) + (9 x 163) + (F x 162) + (D x 161) + (E x 160))10
Step 2 | 19FDE16 | ((1 x 164) + (9 x 163) + (15 x 162) + (13 x 161) + (14 x 160))10
Step 3 | 19FDE16 | (65536+ 36864 + 3840 + 208 + 14)10
Step 4 | 19FDE16 | 10646210

## Slide 13: More examples conversion to decimal
Binary to decimal
101112 = 1×24+0×23+1×22+1×21+1×20 = 16+0+4+2+1= 23
1000112 = 1×25+0×24+0×23+0×22+1×21+1×20 =32+0+0+2+1= 35

## Slide 14: More examples conversion to decimal
Octal to decimal
278 = 2×81+7×80 = 16+7 = 23
308 = 3×81+0×80 = 24
43078 = 4×83+3×82+0×81+7×80= 2247

## Slide 15: More examples conversion to decimal
Hexadecimal to decimal
2816 = 2×161+8×160 = 40
2F16 = 2×161+15×160 = 47
BC1216 = 11×163+12×162+1×161+2×160= 48146

## Slide 16: Conversion table
Decimal Base-10 | BinaryBase-2 | OctalBase-8 | HexadecimalBase-16
0 | 0 | 0 | 0
1 | 1 | 1 | 1
2 | 10 | 2 | 2
3 | 11 | 3 | 3
4 | 100 | 4 | 4
5 | 101 | 5 | 5
6 | 110 | 6 | 6

## Slide 17: Conversion table
Decimal Base-10 | BinaryBase-2 | OctalBase-8 | HexadecimalBase-16
7 | 111 | 7 | 7
8 | 1000 | 10 | 8
9 | 1001 | 11 | 9
10 | 1010 | 12 | A
11 | 1011 | 13 | B
12 | 1100 | 14 | C

## Slide 18: Conversion table
Decimal Base-10 | BinaryBase-2 | OctalBase-8 | HexadecimalBase-16
13 | 1101 | 15 | D
14 | 1110 | 16 | E
15 | 1111 | 17 | F
16 | 10000 | 20 | 10
17 | 10001 | 21 | 11
18 | 10010 | 22 | 12
19 | 10011 | 23 | 13

## Slide 19: Conversion table
Decimal Base-10 | BinaryBase-2 | OctalBase-8 | HexadecimalBase-16
20 | 10100 | 24 | 14
21 | 10101 | 25 | 15
22 | 10110 | 26 | 16
23 | 10111 | 27 | 17
24 | 11000 | 30 | 18
25 | 11001 | 31 | 19

## Slide 20: Conversions from decimal
Decimal to Other Base System
Step 1 − Divide the decimal number to be converted by the value of the new base.
Step 2 − Get the remainder from Step 1 as the rightmost digit (Least significant digit) of the new base number.
Step 3 − Divide the quotient of the previous divide by the new base.
Step 4 − Record the remainder from Step 3 as the next digit (to the left) of the new base number.
Repeat Steps 3 and 4, getting remainders from right to left, until the quotient becomes zero in Step 3.
The last remainder thus obtained will be the Most Significant Digit (MSD) of the new base number.

## Slide 21: Conversions from decimal
DECIMAL TO BINARY
Decimal Number: 2910
Calculating Binary Equivalent
Decimal Number : 2910 = Binary Number : 111012.
Step | Operation | Result | Remainder | Binary result
Step 1 | 29 / 2 | 14 | 1 | 1
Step 2 | 14 / 2 | 7 | 0 | 01
Step 3 | 7 / 2 | 3 | 1 | 101
Step 4 | 3 / 2 | 1 | 1 | 1101
Step 5 | 1 / 2 | 0 | 1 | 11101

## Slide 22: Conversions from decimal
Decimal to Octal
Decimal Number | Operation | Quotient | Remainder | Octal Result
1792 | ÷ 8 = | 224 | 0 | 0
224 | ÷ 8 = | 28 | 0 | 00
28 | ÷ 8 = | 3 | 4 | 400
3 | ÷ 8 = | 0 | 3 | 3400

## Slide 23: Conversions from decimal
DIVISION | RESULT | REMAINDER (in HEX)
256 / 16 | 16 | 0
16 / 16 | 1 | 0
1 / 16 | 0 | 1
ANSWER |  | 100
Ex 1 : Number 256
Decimal to Hexadecimal

## Slide 24: Conversions from decimal
Decimal to Hexadecimal
DIVISION | RESULT | REMAINDER (in HEX)
188 / 16 | 11 | C(12 decimal)
11/16 | 0 | B(11 decimal)
ANSWER |  | BC
Ex 1 : Number 188
DIVISION | RESULT | REMAINDER (in HEX)
590/ 16 | 36 | E (14 decimal)
36 / 16 | 2 | 4
2 / 16 | 0 | 2
ANSWER |  | 24E
Ex 1 : Number 590

## Slide 25: solve #1
Convert FROM DECIMAL
to binary , octal and hexadecimal
Decimal number 100

## Slide 26: results
Step | Operation | Result | Remainder | Binary result
Step 1 | 100/2 | 50 | 0 | 0
Step 2 | 50/2 | 25 | 0 | 00
Step 3 | 25/2 | 12 | 1 | 100
Step 4 | 12/2 | 6 | 0 | 0100
Step 5 | 6/2 | 3 | 0 | 00100
Step6 | 3/2 | 1 | 1 | 100100
Step 7 | 1 /2 | 0 | 1 | 1100100
Decimal to Binary
Decimal to Octal
Step | Operation | Result | Remainder | Binary result
Step 1 | 100/8 | 12 | 4 | 4
Step 2 | 12/8 | 1 | 4 | 44
Step 3 | 1/8 | 0 | 1 | 144

## Slide 27: results
Decimal to hexadecimal
Step | Operation | Result | Remainder | Binary result
Step 1 | 100/16 | 6 | 4 | 6
Step 2 | 6/16 | 0 | 6 | 64

## Slide 28: solve #2
Convert to decimal
Octal number 1000 (ans : 64)
Binary number 1000 (ans : 8)
Hexadecimal number 1000 (ans 4096)

## Slide 29: Non decimal to non decimal conversion
Step 1 − Convert the original number to a decimal number (base 10).
Step 2 − Convert the decimal number so obtained to the new base number.
Example
Octal Number to Binary number: 258
Step 1 − Convert the decimal.
Step | Octal Number | Decimal Number
Step 1 | 258 | ((2 x 81) + (5 x 80))10
Step 2 | 258 | (16 + 5)10
Step 3 | 258 | 2110

## Slide 30: Non decimal to non decimal conversion
Step 2− Convert 21 (decimal) the binary.
Decimal Number : 2110 = Binary Number : 101012
Octal Number : 258 = Binary Number : 101012
Step | Operation | Result | BINARY
Step 1 | 21 / 2 | 10 | 1
Step 2 | 10 / 2 | 5 | 0
Step 3 | 5 / 2 | 2 | 1
Step 4 | 2 / 2 | 1 | 0
Step 5 | 1 / 2 | 0 | 1

## Slide 31: NON decimal to non decimal shortcut methods

## Slide 32: Binary to octal
Step 1 − Divide the binary digits into groups of three (starting from the right).
Step 2 − Convert each group of three binary digits to one octal digit. (as if you are converting them to decimal)
Example
Binary Number − 101012
Step | Binary Number | Octal Number
Step 1 | 101012 | 010 101
Step 2 | 101012 | 28 58
Step 3 | 101012 | 258

## Slide 33: Octal to binary
Step 1 − Convert each octal digit to a 3 digit binary number (the octal digits may be treated as decimal for this conversion).
Step 2 − Combine all the resulting binary groups (of 3 digits each) into a single binary number.
Octal Number − 258
Step | Octal Number | Binary Number
Step 1 | 258 | 210 510
Step 2 | 258 | 0102 1012
Step 3 | 258 | 0101012

## Slide 34: Binary to hexadecimal
Step 1 − Divide the binary digits into groups of four (starting from the right).
Step 2 − Convert each group of four binary digits to one hexadecimal symbol.
Example
Binary Number − 101012
Step | Binary Number | Hexadecimal Number
Step 1 | 101012 | 0001 0101
Step 2 | 101012 | 110 510
Step 3 | 101012 | 1516

## Slide 35: Hexadecimal to binary
Step 1 − Convert each hexadecimal digit to a 4 digit binary number (the hexadecimal digits may be treated as decimal for this conversion).
Step 2 − Combine all the resulting binary groups (of 4 digits each) into a single binary number.
Hexadecimal Number − 1516
Step | Hexadecimal Number | Binary Number
Step 1 | 1516 | 110 510
Step 2 | 1516 | 00012 01012
Step 3 | 1516 | 000101012

## Slide 36: Binary arithmetic

## Slide 37: Binary addition
There are four rules of binary addition.
In fourth case, a binary addition is creating a sum of (1 + 1 = 10) i.e. 0 is written in the given column and a carry of 1 over to the next column.
 | Rule#1 | Rule#2 | Rule#3 | Rule#4
A | 0 | 0 | 1 | 1
+ B | 0 | 1 | 0 | 1
A+B | 0 | 1 | 1 | 0 (CARRY 1)

## Slide 38: Binary addition
 | Rule#1 | Rule#2 | Rule#3 | Rule#4
A | 0 | 0 | 1 | 1
B | 0 | 1 | 0 | 1
A+B | 0 | 1 | 1 | 0 (CARRY 1)

## Slide 39: Binary addition

## Slide 40: Binary subtraction
Subtraction and Borrow, these two words will be used very frequently for the binary subtraction. There are four rules of binary subtraction.
 | Rule#1 | Rule#2 | Rule#3 | Rule#4
A | 0 | 1 | 1 | 0
-B | 0 | 1 | 0 | 1
A - B | 0 | 0 | 1 | 1 (BORROW 1)

## Slide 41: Binary subtraction
BORROW |  | 1 | 1 | 1 | 
A | 1 | 0 | 1 | 0 | 1
-B | 0 | 1 | 1 | 1 | 0
A - B | 0 | 0 | 1 | 1 | 1